## Slide 1: WoT Servient using SmartThings and Iotivity
May 23, 2016

## Slide 2: WoT Servient using SmartThings and Iotivity
Expose SmartThings capabilities as OCF resource types with WoT Thing Description
HTTP, CoAP, and MQTT Protocol Bindings
Uses iotivity as the resource layer
node-iotivity: existing nodejs API and binding
iot-rest-api-server: existing HTTP proxy for iotivity
New nodejs based servient shell provides a client+ server scripting API and abstract transfer layer

## Slide 3: SmartThings + Iotivity WoT Servient
Things
Things
node-iotivity
iotivity
SmartThings
Servient Shell
Scripts
Handlers
Thing Description
WS
HTTP
CoAP
MQTT
Things
iot-rest-api-server
Client - Consumes
Server - Exposes
HTTP
CoAP

## Slide 4: Some Questions
What does a SmartThings TD look like?
What does a SmartThings/OCF Resource Type look like?
Can iotivity expose Thing Descriptions?
How does the action collection pattern work?
How does the subscription pattern work?

## Slide 5: Mapping SmartThings Capabilities
W3C WoT Thing Descriptions
  WoT Thing models a SmartThings Thing, at the device level
  Capability-level granularity would be better for applications and security
OCF Resource Types and Collections
  Attributes and Commands mapped using the WoT Interaction model and abstract transfer binding
  https://github.com/hyperstate/hyperstate-docs/blob/master/wot-18may.pdf
  Resource Directory + device bridge architecture

## Slide 6: Modeling SmartThings Capabilities
Use oneiota to create a canonical model for an abstract SmartThings Capability with attribute and command type mappings to read/write/observe properties and actionInstance collections
It should be fairly easy to create the capability types by customizing the abstract model for capability types
Generate WoT Thing Description templates automatically from Capability Models
Can we bypass oneiota in the chain and construct resource instances from TD instances?

## Slide 7: Use case for SmartThings Models
IoTivity SmartThings Bridge
A SmartThing is a collection of Capabilities
Each Capability has a model
Discover SmartThings Things and construct IoTivity resource instances from capabilities
How does oneiota help?